## Slide 1: Building Embedded Linux with Yocto on Raspberry Pi 4, Deploying Hardware-Accelerated Edge AI and Developing a Device Driver
Ho Chi Minh City, October 2026
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
FACULTY OF ADVANCED TRAINING
FINAL REPORT · COURSE: EMBEDDED SYSTEMS
GROUP 4
Supervisor:
M.Sc. Huỳnh Hoàng Hà
Students:
Đỗ Gia Bảo
Student ID: 23161046
Tô Quốc Hiệp
Student ID: 22161050
Nguyễn Đoàn Hoàng Ngân
Student ID: 24119064
Đặng Nguyễn Nam Nhật
Student ID: 22119022
Tô Ngọc Thảo Uyên
Student ID: 24119098
Notes: Good morning. We are Group 4. Our project builds a custom embedded Linux with Yocto for the Raspberry Pi 4, deploys a MobileNet V1 Edge AI workload on it, and adds a Linux character device driver tested on QEMU.

## Slide 2: Team and task assignment
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Supervisor: M.Sc. Huỳnh Hoàng Hà
No. | Full name | Student ID | Role
1 | Đỗ Gia Bảo | 23161046 | Virtualization, QEMU emulation
2 | Tô Quốc Hiệp | 22161050 | Embedded co-developer
3 | Nguyễn Đoàn Hoàng Ngân | 24119064 | Device driver development, report writing
4 | Đặng Nguyễn Nam Nhật | 22119022 | Team leader
5 | Tô Ngọc Thảo Uyên | 24119098 | Device driver development
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
2 / 17
Notes: Five members. Nam Nhật leads and built the Edge AI part. Quốc Hiệp reproduced the Yocto build and documented the boot flow. Hoàng Ngân and Thảo Uyên wrote the device driver; Hoàng Ngân also wrote the report. Gia Bảo set up QEMU emulation.

## Slide 3: Outline
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
01
Overview
Problem, constraints of embedded systems, research questions and scope
02
Background
The 7-stage, GPU-first boot process of the Raspberry Pi 4
03
System design and implementation
Yocto build for the Raspberry Pi 4, Edge AI software stack, mychardev driver on QEMU
04
Experimental results and evaluation
C vs Python, multi-core scaling, 1,000-image benchmark, bottleneck, driver tests
05
Conclusion and future work
What was achieved, limitations and next steps
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
3 / 17
Notes: The talk follows the five chapters of the report.

## Slide 4: Problem and research questions
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
CONSTRAINTS OF EDGE HARDWARE
Memory scarcity
Limited RAM; Python’s interpreter, dynamic types and garbage collector cost memory
Execution latency
Sensor streams need real-time rates: above 20 frames per second
Thermal and power
Locking cores at maximum clock risks thermal throttling and hardware wear
Black box vs native
Treat the network as deterministic math; compare compiled C with interpreted Python
RESEARCH QUESTIONS
Q1 How to build a minimal, reproducible Yocto Linux for the Raspberry Pi 4 that supports hardware debugging and an Edge AI runtime?
Q2 How does the BCM2711 boot, and how can boot time be measured and optimized?
Q3 Native C vs Python: latency, jitter and peak RSS memory?
Q4 Can multi-core threading reach real time (above 20 fps) without retraining, and where is the bottleneck?
Added by the instructor: QEMU emulation in Yocto and a custom device driver tested on QEMU.
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
4 / 17
Notes: Scope: the Edge AI part runs and is measured on a real Raspberry Pi 4 Model B; the device driver is built and tested only on QEMU (qemux86-64).

## Slide 5: Raspberry Pi 4: the 7-stage, GPU-first boot
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
5 V power on
Stage 1
On-chip BootROM, clock init
GPU
Stage 2
SPI EEPROM bootloader: LPDDR4, EMMC2/USB
GPU
Stage 3
start4.elf, fixup4.dat memory split
GPU
Stage 4
config.txt, DTB, zImage, cmdline.txt
GPU
Stage 5
DTB address → r2, CPU reset released
GPU
Stage 6
Kernel: MMU, GIC-400, drivers, rootfs
ARM CPU
Stage 7
systemd PID 1, udev, getty on ttyAMA0
ARM CPU
Login prompt
Unlike an x86 PC, the VideoCore VI GPU runs Stages 1–5 while the Cortex-A72 cores are held in reset; Stage 5 hands the board over to the ARM CPU.
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
5 / 17
Notes: The BootROM starts the GPU. Since the Pi 4, the second-stage bootloader lives in a 4 MB SPI EEPROM on the board. The GPU firmware start4.elf reads config.txt, loads the device tree and the kernel, writes the DTB address into r2 and releases the CPU. The kernel mounts the root partition, and systemd as PID 1 starts getty on the serial console.

## Slide 6: Building Yocto Linux for the Raspberry Pi 4
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
1. Prepare host
apt install build deps; locale-gen en_US.UTF-8
2. Fetch sources
git clone -b scarthgap: Poky + meta-raspberrypi
3. Configure
local.conf: MACHINE, INIT_MANAGER, ENABLE_UART, rm_work
4. Build image
bitbake core-image-base (5,806 tasks)
5. Inspect image
bzcat → .wic (329 MB); losetup + mount the 2 partitions
6. Write SD card
dd bs=4M conv=fsync, then sync
7. Boot and debug
UART on GPIO 14/15, picocom at 115,200 baud
Build system | Tasks | Build size | Disk image | Kernel | Init | RAM when idle
Poky 5.0.20 “Scarthgap” (LTS) | 5,806, all succeeded | ~28 GB with rm_work | 329 MB WIC, 2 partitions | 6.6.63-v7l, ARMv7l SMP | systemd | ~55 MB of ~3.9 GB
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
6 / 17
Notes: Host: Ubuntu 22.04 in VMware. If a build fails, we read the log, run bitbake -c cleansstate on the failing package and rebuild. The 329 MB WIC image has a 130 MB FAT32 boot partition and a 192.4 MB ext4 root partition; /sbin/init links to systemd. Tô Quốc Hiệp independently reproduced the build on a 50 GB host, which confirms it is reproducible.

## Slide 7: Edge AI software stack on the Raspberry Pi 4
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Input data: model.tflite (4.1 MB), input.bin, imagenette1000_rgb224_u8.bin.gz (100.5 MB)
Python application
benchmark_1000_python.py
Native C application
benchmark_1000_c (ARM ELF)
python3-tensorflow-lite, python3-numpy
libtensorflowlite_c.so, zlib
Yocto Linux
Poky 5.0.20 – kernel 6.6.63 – systemd – ttyAMA0 (UART)
Raspberry Pi 4 Model B
BCM2711 (4 × Cortex-A72, 1.5 GHz) – 4 GB LPDDR4
Layer meta-edge-ai
A .bbappend for libtensorflow-lite-c 2.16.2 installs the C API headers (c_api.h, c_api_types.h, builtin_ops.h).
Model and data
MobileNet V1, uint8-quantized: 4.1 MB, 75% smaller. Input [1, 224, 224, 3]; 1,000 Imagenette images, 10 classes.
Two engines
Python (tflite_runtime) and native C (TFLite C API + zlib) run the same workload.
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
7 / 17
Notes: On top of the Yocto image we added meta-tensorflow-lite, meta-openembedded and our own layer meta-edge-ai. Quantization maps float32 weights to 256 integer levels, so the model shrinks from about 16 MB to 4.1 MB and integer math runs faster on the Cortex-A72. Both engines are cross-compiled by Yocto; the C programs are 32-bit ARM ELF files.

## Slide 8: mychardev: from source code to QEMU
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Source: mychardev.c, Makefile, COPYING
Compile with Kbuild → mychardev.ko
Install to …/lib/modules/…/updates/
Package: kernel-module-mychardev, mychardev
Add to rootfs.ext4 (core-image-minimal)
Boot QEMU: auto-load → /dev/mychardev
do_fetch, do_unpack
do_compile
do_install
do_package, do_package_write_rpm
do_rootfs (IMAGE_INSTALL)
KERNEL_MODULE_AUTOLOAD
mychardev at a glance
Misc device: major 10, minor 259 (dynamic)
/dev/mychardev, permissions 0666
1024-byte kernel buffer, protected by a mutex
open, read, write, release, llseek
Out-of-tree module; recipe inherits module
QEMU + KVM: qemux86-64, kernel 6.6.151
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
8 / 17
Notes: Left: each step from source code to the running virtual machine; right of each box is the BitBake task that does it. The driver lives in its own layer, meta-mydriver. It registers a misc device, so one misc_register call creates /dev/mychardev. Read and write use simple_read_from_buffer and simple_write_to_buffer under a mutex. runqemu qemux86-64 nographic slirp kvm boots a q35 machine with 4 cores and 256 MB RAM; SSH is forwarded on port 2222.

## Slide 9: Single image: native C vs Python (1 thread)
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Both engines predict “military uniform” (class 653, score 227, 89.02% confidence) on the Grace Hopper image.
Metric | Python | Native C | Assessment
Mean inference latency | 161.113 ms | 160.320 ms | C 0.793 ms faster (0.49% lower)
Median latency | 160.397 ms | 160.297 ms | Difference of 0.100 ms (0.06% lower)
95th percentile (P95) | 162.791 ms | 160.539 ms | C has a tighter tail (2.252 ms lower)
Peak RAM (RSS) | 31.37 MiB | 10.12 MiB | C saves 21.25 MiB (67.7% less memory)
Predicted class | 653 (score 227) | 653 (score 227) | Exact mathematical match
Same speed, much less memory: the heavy math runs in the shared TensorFlow Lite C++ library; Python’s overhead is the interpreter’s memory.
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
9 / 17
Notes: Latency is almost identical, about 160 ms, because both engines call the same TensorFlow Lite kernels. The real difference is memory: 31.37 MiB for Python against 10.12 MiB for C.

## Slide 10: Multi-core scaling: 1, 2 and 4 threads
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Threads | Python | Native C | Speedup (C) | CPU usage
1 thread (1 core) | 161.030 ms | 159.138 ms | 1.00× (baseline) | 99.93% (1 core)
2 threads (2 cores) | 83.459 ms | 82.799 ms | 1.92× | 199.89% (2 cores)
4 threads (4 cores) | 44.219 ms | 43.326 ms | 3.67× | 398.98% (4 cores)
3.67×
speedup of native C with 4 threads, close to the ideal 4×
72.8%
lower latency for C (72.5% for Python), no retraining or pruning
~4 cores
CPU usage grows almost linearly, from 99.93% to 398.98%
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
10 / 17
Notes: Only the num_threads parameter changes; the model weights stay the same. Going from 1 to 4 threads cuts latency from about 160 ms to about 44 ms, a 3.65 to 3.67 times speedup.

## Slide 11: Benchmark on 1,000 Imagenette images
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Metric | Python, 1 thread | Native C, 1 thread | Python, 4 threads | Native C, 4 threads
Total time (1,000 images) | 164.399 s | 162.040 s | 47.184 s | 46.402 s
Mean inference latency | 161.011 ms | 159.312 ms | 43.957 ms | 43.672 ms
Throughput | 6.083 images/s | 6.171 images/s | 21.193 images/s | 21.551 images/s
CPU usage | 99.89% | 99.93% | 390.20% | 394.07%
Peak memory (RSS) | 33.72 MiB | 10.25 MiB | 33.72 MiB | 10.25 MiB
21.55/s
native C, 4 threads: above the 20 images/s target
~71%
less total time with 4 threads: ~164 s → 46–47 s
30.4%
of Python’s memory for C (10.25 vs 33.72 MiB)
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
11 / 17
Notes: All 1,000 validation images were run with 1 and 4 threads on both engines. Python with 4 threads reaches 21.19 images/s. A line-by-line check of all 1,000 predictions found zero differences, so threading does not change the classification.

## Slide 12: Bottleneck: inference dominates each image
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
1. Read and decompress
(zlib / gzip)
2. Copy input tensor
3. Inference
(MobileNet V1)
4. Post-processing
(Top-1, Top-5)
2.658 ms
0.060 ms
159.312 ms (98.32%)
0.006 ms
Per image | Python, 1 thread | Native C, 1 thread | Python, 4 threads | Native C, 4 threads
Total latency | 164.329 ms | 162.036 ms | 47.117 ms | 46.398 ms
Inference (MobileNet) | 161.011 ms | 159.312 ms | 43.957 ms | 43.672 ms
Share of inference | 97.98% | 98.32% | 93.30% | 94.12%
Times under the boxes: native C, 1 thread. Reading, copying and post-processing take under 6.7% of the time, so CPU arithmetic is the bottleneck and multi-core threading is the best lever.
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
12 / 17
Notes: We timed the four stages of every image separately. Inference takes 93.30% to 98.32% of the time in every configuration, so optimizing file reading or tensor copying would barely matter.

## Slide 13: CPU governor and model accuracy
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Configuration and metric | ondemand | performance | Impact
Python 4 threads: mean latency | 44.011 ms | 43.860 ms | −0.151 ms (0.34% better)
Python 4 threads: total time | 47.402 s | 47.012 s | −0.390 s (0.82% better)
Native C 4 threads: mean latency | 43.581 ms | 43.607 ms | +0.026 ms (statistical noise)
Native C 4 threads: total time | 46.316 s | 46.325 s | +0.009 s (negligible)
Operating temperature | 46.2 → 61.8 °C | 65.2 → 70.6 °C | 8.8 to 19.0 °C hotter
ondemand
kept: performance gains under 1% but runs hotter
69.10%
Top-1 accuracy: 691 of 1,000 Imagenette images
0
discrepancies: all 8 configurations predict the same classes
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
13 / 17
Notes: ondemand scales the clock from 600 MHz to 1.5 GHz; performance locks all four Cortex-A72 cores at 1.5 GHz. The gain is under 1%, so we restored ondemand. Per-class accuracy ranges from 32% (Church) to 91% (Tench, Golf Ball). Parameters and hashes are stored in experiment_record.txt.

## Slide 14: Testing the mychardev driver on QEMU
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
No. | Test command | Expected result | Result
1 | lsmod | The mychardev module has been loaded | Pass
2 | modinfo mychardev | Correct version, description, updates/ path | Pass
3 | ls -l /dev/mychardev | Character device, major 10, permissions rw-rw-rw- | Pass
4 | echo ... > /dev/mychardev | Write succeeds, dmesg records the number of bytes | Pass
5 | cat /dev/mychardev | Reads back exactly the string that was written | Pass
6 | rmmod mychardev | /dev/mychardev is removed | Pass
7 | modprobe mychardev | Reloads successfully, /dev/mychardev reappears | Pass
dmesg shows the call order opened → wrote 19 bytes → closed: the 18 characters of “Xin chao tu Yocto!” plus the newline added by echo.
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
14 / 17
Notes: The build ran 4,657 tasks, 4,552 of them from sstate-cache. The kernel loads mychardev at second 1.72 during boot thanks to KERNEL_MODULE_AUTOLOAD. Known limits: no O_TRUNC handling, writes past 1024 bytes return 0 instead of -ENOSPC, and the buffer is static.

## Slide 15: Objectives versus results
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Objective | Result achieved | Status
Q1: custom Yocto build for the Raspberry Pi 4 | Built core-image-base (5,806 tasks), 329 MB WIC image, boots successfully with systemd, with UART debugging | Completed
Q2: boot architecture of the BCM2711 | Detailed description of the 7-stage GPU-first boot process, with a table of boot files | Completed
Q3: native C versus Python | Equivalent latency (about 160 ms), C reduces RSS memory by 67.7% to 69.6% (10.12 vs 33.72 MiB), 100% matching predictions | Completed
Q4: multi-core acceleration, system bottleneck | 3.67× speedup with 4 threads, throughput of 21.55 images/s; inference accounts for 93.30% to 98.32% of the time | Completed
QEMU emulation and device driver | Built for qemux86-64; the mychardev driver loads automatically at boot and passes all 7 test cases | Completed
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
15 / 17
Notes: All four research questions and both added objectives were completed.

## Slide 16: Conclusion and future work
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY AND ENGINEERING
Faculty of Advanced Training
EMBEDDED SYSTEMS
Conclusion
Custom Yocto Linux (Poky Scarthgap) boots the Raspberry Pi 4 from a 329 MB WIC image with systemd and UART debugging
The 7-stage, GPU-first boot of the BCM2711 is fully documented
Native C matches Python’s latency (~160 ms) with 67.7–69.6% less RSS memory
4 threads: 3.67× faster, 21.55 images/s; Top-1 69.10%, 0 discrepancies
mychardev auto-loads on QEMU and passes all 7 tests
Limitations and future work
Measure on-board JPEG decoding and resizing, run more repetitions, add power measurements
Shorten boot time with systemd-analyze and systemctl mask
Driver: handle O_TRUNC, report buffer overflow, dynamic buffer; add ioctl, sysfs/procfs, poll/select
Real hardware: platform driver + Device Tree (e.g., GPIO); test on qemuarm/qemuarm64 first
AI performance on the board improved without changing the model’s structure or weights, and the whole system is reproducible from configuration files and recipes.
Group 4 · Embedded Linux, Edge AI and a device driver on Raspberry Pi 4
16 / 17
Notes: Limitations: tensors were preprocessed on Ubuntu, so on-board JPEG decoding is not measured; repetitions are limited and power was not measured. The driver is a virtual device tested only on QEMU.

## Slide 17: Thank you for listening!
Questions and answers
Group 4 · Embedded Systems · Ho Chi Minh City, October 2026
Notes: Thank the supervisor, M.Sc. Huỳnh Hoàng Hà, and open the floor for questions.